Q250M3 VER:1.0A正面图

Q250M3 VER:1.0A IO图

Q250M3 VER:1.0A 侧面图

| Product model | Q250M3 VER:1.0A(I210AT) |
| --- | --- |
| processor | 6th/7th/8th/9th Celeron/Pentium/Core™ i3/i5/i7 processors supporting the LGA1151 architecture, Note: Support 6/7/8/9 generation 95W CPU |
| chipset | Intel Q250 high-speed chipset |
| Internal memory | 2 x DDR4 DIMM slots for dual-channel 2133 MHZ memory, 2400 MHZ memory, and 2666 MHZ memory, with a maximum capacity of 64GB Integrated Intel® HD Graphics controller with 1*VGA port and 1*HD OUTPUT1.4 port |
| display | Supports single display, dual display mode, and extended mode |
| network | 2* Intel I210AT Gigabit network adapter, supporting network wake up and PXE functions |
| deposit | 4* SATA3.0 hard disk interface,SATA transmission speed up to 6Gbps |
|  | 1* MSATA interface, support Intel protocol SSD, transmission rate up to 6Gbps |
|  | 1* M.2 slot, supporting the M.2 2280 PCIE x4/SATA adaptive standard SSD |
| Tone frequency | Onboard ALC888S high fidelity audio controller, support Mic, Line out, line-IN |
| Expansion slot | 1 x PCIE x16 slot |
|  | 1 x PCIE x4 slot |
|  | 2* PCI slot |
| I/O ports on the backplane | 1* PS/2 keyboard and mouse interface |
|  | 1 x VGA display port |
|  | 1*HD OUTPUT display interface |
|  | 2* RS232 serial port (COM1/2 supports 5V/12V live function,COM1/2 supports RS485/422 function) |
|  | 2* RJ45 Gigabit network interface |
|  | 2* USB 2.0 port |
|  | 4* USB 3.0 interface |
|  | 1*Line out interface (green), 1* Mic interface (red), 1* Line-IN interface (blue) |
| Built-in I/O interface | 1* PS/2 keyboard and mouse interface 1*6pin row pin and UK1 signal |
|  | 1* JVGA port 1*12pin pin row, same signal as DB15 |
|  | 4 x RS232 serial port 2 x 5pin row pins |
|  | 1* front audio interface 2*5pin row pins |
|  | 4* USB 2.0 port 2*5Pin row pins |
|  | 1*USB2.0 port USB TYPE-A |
|  | 1* TPM port 2*8pin row pins |
|  | 1* Front panel function buttons and indicator ports 2*5pin row pins |
|  | 1*LPT 2*13 pin row |
|  | 1* 24pin ATX power input interface |
|  | 1* 8pin ATX power input interface |
| Fan interface | 1*4pin CPU intelligent fan interface, 3* 4pin system intelligent fan interface |
| BIOS | 64Mb Flash ROM |
| Operating system | Windows 7 / 10 / Linux |
| Guard dog | Support hardware reset function (256 level, 0~255 seconds) |
| Power supply type | ATX power input |
| Operating temperature | 0℃ to 60℃ |
| Storage temperature | -20℃ to 70℃ |
| Working humidity | 5%-95% relative humidity, no condensation |
| dimension | 245mm x 220mm(mATX) |

# 订购信息：

| No. | Model | Processor | Southbridge | Memory | VGA | HD OUTPUT | LAN | USB | COM | RS485/RS422 | Power |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Q250M3 VER:1.0 | LGA1151 | Q250 | 2*DDR4 | 1 | 1 | 2*I211AT | 11 | 6 | 2 | ATX |
| 2 | Q250M3 VER:1.0(I210AT) | LGA1151 | Q250 | 2*DDR4 | 1 | 1 | 2*I210AT | 11 | 6 | 2 | ATX |

# Text boxes

Q250M3 VER:1.0A 规格表